TYPICAL WIREING SCHEMATIC

From the Power supply to the RGB Controller to the RGB LED

# Wiring your RGB Piling Caps

Make sure all wire connections are waterproof and you match each color of the four wires that you are connecting:

R=red G=green B=blue

The black wire is used for the power V+ as shown on the schematic. This wire can be any color like white black or yellow.

Remember to wire V+ at the controller with the black wire provided to the color you have chosen to use as your V+. Do not exceed more than 200 foot wire runs to your last RBG cap. 18-4 stranded marine grade wire and or shielded wire can be used for your installation on the RGB units

All of are LEDS and controllers run off 12vDC only and our power supplies run off 120vac and converts down to 12vdc