Typical Installation of Illuminating Dock-Caps

Mounting: measure the diameter of your pilings. Not all caps will fit, make sure you purchase the size that is the closest to the diameter of the piling or they can be larger than the piling, the LEDs are sealed. You may need to chisel some around the piling. Use stainless steel screws to secure cap. Run wire in and out of pilings connecting to each cap in a daisy chain

Wire runs: 200 feet per run max on the natural white and under 150 feet per run on the RGB color. (Multi strained 18-2 or 18-4 can be used. RGB requires 4 wires red, green, blue, and a line wire, black or yellow. On your RGB controller you will find marked connectors R-G-B-V. Natural white only 2 wires red + black.

Make all connections with waterproof wire nuts

Wattage: Each Illuminating Dock Cap emits around 2 watts, RGB 2.5 watts and natural white with down light 3 watts (Total all Caps to determine the wattage on the power supply do not exceed 80 % of total watts on power supply).

Do not install any other lights or components with our systems. For further assistance please call Benfive Lighting 772-240-8014